CSCE 574
Section 001
Fall 2017
Project 3 Grid Mapper
Ian Davis

Description

The objective of this project was to implement a ros node that would generate an occupancy grid from laser scan data obtained by a robot in stage. I used the square.world stage for the testing of my grid mapper. I achieved this by 1. moving the robot around the world by using key presses and 2. by turning laser scan data into a point cloud and then converting the points into a coordinates on the robots coordinate frame. I performed the grid mapping by converting the laser scan messages into point-clouds and then obtaining the x and y points from those clouds. I then used those points together with the robots heading to perform 2d rotation transforms. I then performed 2d translation transforms on those points to calculate the coordinates of the obstacle the laser scan received at that specific angle/iteration. I used Bresenham's line drawing algorithm to plot the free space between the robot and the obstacles. I had to look up some code to help with handling all octants that the laser scan covers. One important thing I noticed was when the canvas was a one-to-one ratio with the size of the stage world it was far too inaccurate considering many cells were half occupied but the grid has only free or occupied. So, I multiplied all coordinates by a factor of 10 as well as the canvas length and width so as to increase the accuracy by a factor of 10. with this, the map is much more accurate. Thus by increasing the overall number of cells you decrease the amount of space each cell on the canvas takes up creating a more accurate occupancy grid.

Evaluation
Overall I believe my grid mapper works well. I draws the overall obstacles/wall very well as does the line drawing algorithm. I believe a problem with my grid mapper is that I haven’t implemented a way of preventing the node from overwriting old cells such as the line drawing algorithm overwriting the path the robot takes. The line drawing algorithm also occasionally overwrites some of the occupied space. I don’t know of an easy way to combat this other than manually keeping track of each coordinate I have plotted and checking this reference before plotting each new cell. I don’t know of a way to pull data from the canvas either; to check if the cell has been plotted beforehand. Another issue I have as of writing this report is that the plotting becomes very inaccurate while the robot is turning. I suspect this has many causes: there is no filter being used on the sensor data when I convert it to point-cloud and so it can’t filter out extraneous data, the robot turns faster than the laser data can update so values are plotted too late….etc. I contemplated turning of the plotting while the robot was turning but I felt that merely ignored the problem so I left it as is.

When the node is first started this is what the grid looks like.

When the robot drives straight until it can see the opposite wall.

This is an example of when the robot has scanned the entire square container it is in. This also shows the inaccurate plots that are generated when the robot turns as well as the overwritten robot path by the line drawing algorithm.

Allocation of Effort
 I wrote my code and implemented it as this was the solo portion of the project.